## Slide 1: MASSAVE4 CYCLING SAFETY ORDINANCE PROJECT
Community Meeting
March 2022
DUDLEY TO BEECH
ROSELAND TO WATERHOUSE

## Slide 2: Welcome
Welcome
Project Presentation 6:00-6:20PM
Introductions 6:20 to 6:25
Question and Answer 6:25-8:00 PM
  Presentation and survey available on the project webpage: cambridgema.gov/MassAve4A

## Slide 3: Virtual Meeting Instructions
Use "Raise Hand" button to signal you have a question or press *9 if you are joining by phone only
  Verbal questions will be taken in order hands are raised
  Questions/comments limited to 1 minute to allow as many people as possible to participate
  We will take 10 to 15 questions/comments at a time
Write in questions in Q&A Window
  Questions may be submitted at any time
  Will answer as many questions as possible during Q & A
Will alternate between verbal questions and responses to written questions
Please be kind to each other and help us hear from as many people as possible
Technical support: Wally Joseph (wajoseph@cambridgema.gov)
Bottom Panel of Zoom Screen

## Slide 4: QUESTIONS SUBMITTED IN ADVANCE OF MEETING

## Slide 5: If the MBTA is proposing to remove the overhead wires, why is the project still talking about them as a conflict?

## Slide 6: How does the City Council order regarding an economic analysis of bike lanes affect this project?

## Slide 7: Why are the goals of the project limited to those listed on the project page? What about business access, parking and street trees?

## Slide 8: Why is a two-way bike lane on one side infeasible? Wouldn't it allow more parking to be retained on Mass Ave? Parking on only one side requires drivers and passengers to cross the street more often. Why is one more acceptable than the other?

## Slide 9: Why isn't full build being proposed?

## Slide 10: MEETING CONCLUSION

## Slide 11: Next Steps
Get feedback on DRAFT Recommendation
Obtain City Council approval of Partial Construction recommendation and timeline by April 30, 2022
  If approved, additional public engagement will be completed as the detailed design is developed
If approval is not granted, the corridor must be implemented as a quick-build by April 2024 in accordance with requirements of the CSO
Feasibility Study
Concept Design
Final Design
Construction
NOV 2021
TODAY
COUNCIL MEETING
WE ARE HERE
Public Engagement Events

## Slide 12: Tell us what you think!
Let us know:
Did we miss anything?
What are your thoughts about our DRAFT Recommendation to proceed with Partial Construction?
Complete the survey on the project webpage: cambridgema.gov/MassAve4A Attend the Community Meeting on Thursday, March 3rd 6pm-8pm on Zoom
Join City staff in person on Saturday, March 19th
10am-2pm outside Lunder Arts Center (1801 Mass Ave)
Email the project team at: kriley@cambridgema.gov

## Slide 13: MASSAVE4 CYCLING SAFETY ORDINANCE PROJECT
Informational Video
March 2022
DUDLEY TO BEECH
ROSELAND TO WATERHOUSE

## Slide 14: Purpose of Video
This video will share:
  The project timeline as it relates to the Cycling Safety Ordinance requirements
  What we heard from the public during engagement events in November
  The range of cross section possibilities as well as feasibility considerations for each
  The draft approach to be presented to City Council for consideration
  How to provide feedback to the project team
  Next Steps

## Slide 15: What drives our street design?
We design for people of ALL ages and abilities. This means including:
People who many not have access to a car
Safe and accessible facilities, including bike lanes, that can be used by a wide range of people
How we think about vehicle congestion and delay
Moving people slowly is moving people safely
We do not prioritize eliminating delay for people driving alone
Many policies and plans are foundational to our work
1) 1992 Cambridge Vehicle Trip Reduction Ordinance, 2) 1993/2007 Cambridge Growth Policy, 3) 2016 Complete Streets Policy, 4) 2016 Vision Zero Policy
Focus is on moving people and goods, not their vehicles
Buses run less frequently than cars and carry more people
Cannot ignore access for trucks and local deliveries

## Slide 16: Why Separated Bike Lanes?
Fewer crashes
Eliminates threat of “dooring” from parked vehicles
Buffer space reduces conflicts between turning vehicles and people biking
Shorter crossing distances for people walking
Increased comfort for people biking of all ages and abilities
Increased comfort for people driving as they know where to expect people biking
Enables more people to choose cycling as a transportation option
Supports City’s climate goals

## Slide 17: Project Background
Cambridge Cycling Safety Ordinance (CSO) requires separated bike lanes along Mass Ave
For MassAve4 - by April 30, 2022 the City must:
  Present analysis on which sections can be quick-build or construction
  Obtain approval from the City Council on a construction timeline for separated bike lane sections not recommended for quick-build
Any sections recommended for quick-build must be installed by April 30, 2023
If a timeline is not approved by the City Council for sections recommended for construction, those sections must be quick-build and installed by April 30, 2024

## Slide 18: Study Area
There are many installed, planned and ongoing projects along Mass Ave
This study is reviewing the MassAve4 segments with overhead wires, including:
  Dudley Street to Beech Street
  Roseland Street to Waterhouse Street
Notes: Update color of installed segments to green

## Slide 19: MBTA Overhead Wires
Overhead wires power trackless trolley buses along Mass Ave
Overhead wires present design challenges for access to buildings by the fire department
Design options must ensure no conflicts between ladder trucks and overhead wires
Notes: Include unclear timelines in script

## Slide 20: MBTA Overhead Wire Status
Beginning March 2022, MBTA will de-energize the overhead wires on Mass Ave for five years to accommodate construction projects in Cambridge and Watertown
MBTA is proposing to convert the trolley buses to Battery Electric Buses (BEBs) and remove the overhead wires. The timeline for removal is currently unknown
Removing the overhead wires provides significantly more flexibility for design options
Notes: Include unclear timelines in script

## Slide 21: Design Opportunities
Recall the three levels of construction that could be considered:
  Quick Build – paint and flex posts, maintain median and sidewalks
  Partial Construction – removal of center median, paving and upgrades to affected utilities
  Full Construction – median removal, street/sidewalk reconstruction and full utility upgrades

## Slide 22: Public Engagement Summary November 2021

## Slide 23: Public Engagement: Overview
Four pop-up events in November
1400+ recorded comments
200+ survey respondents
(through 11/30/2021)
St. John’s Church
location
Cambridge Common
location
Notes:   Saturday, November 13th
    St. John’s Church
    Cambridge Common
  Monday, November 15th
    St. John’s Church
  Tuesday, November 16th
    Cambridge Common
1,400+ comments =number of dots on boards and number of comments/dots on maps
Exact # of survey responses through 11/30 is 233

## Slide 24: Public Engagement: Common Themes
“I love all the shops and restaurants”
“I love seeing people walk around and eat outside”
“We need separated bike lanes”
“Crossing Mass Ave is extremely frightening”
“Please… retain parking to help small businesses survive”
“Parking for us will be challenging if taken away”
“Bike travel is much more dangerous than it should be”
“Consider the needs of … elderly and disabled in the area”

## Slide 25: Public Engagement Themes
Provide Customer Parking
Reconsider the Median
Expand Separated Bike Lanes
Improve experience for people walking and taking the bus

## Slide 26: Option Feasibility Review

## Slide 27: Feasibility Considerations
There are many possible configurations for Mass Ave based on the available space
For these segments of Mass Ave, special consideration for emergency and fire access is required due to the median and overhead wires
Other considerations include:
  Safety for people walking
  Safety for people biking
  Transit efficiency
  Parking/curbside access for businesses
  Utility impacts
  Implementation timeline

## Slide 28: Infeasible Options
Several options were reviewed but deemed infeasible and therefore not advanced:
  Parking along the median
  Bike or bus lanes along the median
  Two-way bike lane on one side
  Wider landscaped median
  One lane and parking on each side with median
  Two lanes and parking on each side without median
These options do not:
  Allow for safe and intuitive use of the street by all users;
  Allow emergency services to travel down the corridor and access buildings unimpeded; and/or
  Fit within the available space.

## Slide 29: Quick-Build Options Existing Median Maintained
Center median removal, customer parking, and separated bike lane options generated high interest
Two Travel Lanes
Travel Lane and Bus Lane
FEASIBLE
Allows for emergency and fire access. Requires removal of parking along the corridor
FEASIBLE
Allows for emergency and fire access. Requires removal of parking along the corridor

## Slide 30: Partial Construction Options Existing Median Removed/Modified
One Travel Lane with Painted Median/Turn Lane
FEASIBLE
for small segments if overhead wires are removed. Not compatible with bus lanes
Travel Lane and Bus Lane with Parking on one side
FEASIBLE
Parking can change sides along the corridor. More design flexibility if overhead wires are removed.
Two Travel Lanes with Parking on One Side
FEASIBLE
Parking can change sides along the corridor. More design flexibility if overhead wires are removed.

## Slide 31: Full Construction Options Median Removed and Sidewalks Reconstructed
Two Travel Lanes with Parking on One Side
Travel Lane with Bus Lane and Parking on One Side
FEASIBLE
Parking can change sides along the corridor. More design flexibility if overhead wires are removed.
FEASIBLE
Parking can change sides along the corridor. More design flexibility if overhead wires are removed.
Center-running Bus Lanes
FEASIBLE
Requires long-term investments. Parking limited to one side between bus stops and intersections
Notes: Remove buffer and add space to boarding island

## Slide 32: Feasible Option Summary
Median Maintained
Parking removed for emergency access
May include bus lanes for all or part of the corridor
Median Removed
Parking on one side of street (may change sides as needed)
May include bus lanes for all or part of the corridor
Additional design flexibility if overhead wires are removed
Quick Build
Partial & Full Construction

## Slide 33: Possible Design Features

## Slide 34: Improvements for people biking
Quick Build
Partial Construction
Full Construction
Flex posts and paint
Flex post or concrete curb barrier separation
Raised sidewalk-level bike lanes
Notes: Quick build and partial build bike lanes will have similar separation

## Slide 35: Improvements for people walking
Quick Build
Partial Construction
Full Construction
Refresh existing crosswalks
Leading Pedestrian Intervals (LPIs)
Reconstruct crossing islands and accessible pedestrian ramps
Leading Pedestrian Intervals (LPIs)
Reconstruct islands and ramps
Raised side street crossings
Add trees and landscaping
Notes: Accessibility?

## Slide 36: Improvements for people taking the bus
Quick Build
Partial Construction
Full Construction
Floating bus islands
Center bus lanes
Bus Lanes
Transit Signal Priority/Queue Jumps
Bus Lanes
Transit Signal Priority/Queue Jumps

## Slide 37: Curbside Use
Quick Build
Partial Construction
Full Construction
Off-peak loading
Accessible parking
Short term and accessible parking
Outdoor dining
Loading zones
Short term and accessible parking
Outdoor Dining
Loading zones
Add photo of outdoor dining

## Slide 38: Utility and Signal Considerations
Quick Build
Partial Construction
Full Construction
Minor signal upgrades
Spot repaving
Signal relocation/upgrades
Upgrades to affected utilities
Full signal upgrades
Major utility upgrades

## Slide 39: Option Evaluation

## Slide 40: Quick Build Summary
Flex-post bike lane separation
0-5% parking maintained
Lowest impact on utilities
Shorter implementation timeline (1 year)
Lower cost ($)
Public Engagement Themes
Separated Bike Lanes
Improvements for people walking and taking the bus
Provide Customer Parking on Mass Ave
Remove the Median
Meets CSO goal of accelerated separated bike lane implementation

## Slide 41: Partial Construction Summary
Flex-post or Curbed bike lane separation
Median removed, but upgraded at pedestrian crossings
Upgrade affected utilities
40-50% parking possible to maintain (if wires are removed)
Medium implementation timeline (to be determined based on project scope and utilities)
Medium cost ($$)
Public Engagement Themes
Separated Bike Lanes
Improvements for people walking and taking the bus
Provide Customer Parking on Mass Ave
Remove the Median
Meets CSO goal of accelerated separated bike lane implementation
Notes: Timeline to be developed for consideration by Council

## Slide 42: Full Construction Summary
Raised bike lane separation
Median removed, but maintained and upgraded at pedestrian crossings
Sidewalk reconstruction and new plantings/amenities
Major utility upgrades
40-50% parking possible to maintain (if wires are removed)
Longer design and implementation timeline (10+ years)
Higher cost ($$$$)
Public Engagement Themes
Separated Bike Lanes
Improvements for people walking and taking the bus
Provide Customer Parking on Mass Ave
Remove the Median
Meets CSO goal of accelerated separated bike lane implementation

## Slide 43: DRAFT Recommendation
Based on community feedback and the analysis completed, the Partial Construction option of removing the median is recommended
This option meets CSO goals, can maintain up to 40-50% of existing parking (if overhead wires are removed) and allows for improvements for people walking, biking and taking the bus