## Slide 1
Dodge Street
Western Ave to Callender St
Reconstruction Project

## Slide 2: Dodge Street

## Slide 3
Chestnut Street Sidney Street to Pleasant Street
Reconstruction Project

## Slide 4: Construction Project Scope
Reconstruct/repave street
Reconstruct sidewalks and curb ramps
New crosswalks, pavement markings
Evaluation and updating utilities
Project Objectives
Meet access codes
Improve safety for all users
Enhance appearance of the neighborhood
Enhance green areas/new trees

## Slide 5
Safety first !!

## Slide 6: GUIDING PLANS AND POLICIES
In addition to Complete Streets and Vision Zero
Cambridge Growth Policy emphasizes sustainable modes of transportation such as walking, biking and using transit and low-emission vehicles, which promote livability and help to improve air quality and reduce greenhouse gas emissions (1993/2007).
Vehicle Trip Reduction Ordinance established programs to encourage alternatives to single-occupancy vehicle travel (1992).
Notes: In addition to Complete Streets and Vision Zero, the city has several other policies and plans that form the basis of our approach to street reconstruction.
Policies – Cambridge Growth Policy and Vehicle Trip Reduction Ordinance – emphasis on sustainable modes of transportation to promote livability, improve air quality and reduce gas emissions.
Pedestrian Plan, Bicycle Plan and Transit Plan – emphasis on how to improve comfort, safety and operation for sustainable modes of transportation.
Goal is to provide a transportation system that is sustainable and efficient; moving people safely.
Climate Plan and commitment to urban forest (street trees) – important commitments for a changing environment,
slow down climate change by lowering greenhouse gas emissions
and reduce impacts of climate change (provide increased tree canopy to reduce impacts of increasing heat waves.
Use these policies and plans to provide basis for design process. Then work with residents on detailed design options.

## Slide 7
International or “zebra” striping
Mark all legs of an intersection
Thermoplastic or inlay tape
Making crossings work
Curb extensions reduce crossing distances
and improve visibility

## Slide 8: Pedestrian injuries/Fatalities in Crashes by Vehicle Speed

## Slide 9
Access

## Slide 10
Green Curb Extension

## Slide 11: Traffic Calming Tools
• Narrow the road
Add Parking
Pavement Markings (edge line for bikes)
Visual Narrowing by Adding Trees
• Horizontal Devices: make the road less straight
Chicanes
Crossing Islands
• Vertical devices: make vehicles go over something
Raised intersections & crosswalks

## Slide 12: Raised intersection

## Slide 13
Raised intersections reduce vehicle speed, improves accessibility
and improves visibility
Raised Intersection

## Slide 14: Curb extension

## Slide 15: Curb extension
Curb extensions reduces crossing distance, improves accessibility, prevents vehicles from parking too close to the intersection
and improves visibility

## Slide 16: Service and Emergency vehicles

## Slide 17
CHESTNUT STREET Reconstruction – First Meeting held 5/9/2019
Community Feedback:
Vehicles traveling too fast*
Too many trucks – too big*
Trucks going to fast*
Roadway in bad condition – Potholes
Noise*
Vehicles turning too fast into Chestnut Street from Magazine*
Sidewalks in poor condition
Utility poles – to be evaluated
Poor drainage*
Pearl Street crashes
Sidewalk access concerns
Safety concerns – Day care
* Repeated Concern

## Slide 18: How did we develop the plans we are presenting today?
DESIGN PROCESS:
Community Input
City/State/Federal policies
Walk with City Arborist to:
  Evaluate condition of existing trees
  Identify possible location for new street trees
Data collection:
  Speed
  Traffic volume
  Crash
Meet with Fire Department to discuss:
  Potential raised intersection (Fire Chief)
  Potential Curb extension

## Slide 19: Speed data
Chestnut Street – East of Whitney Avenue
Chestnut Street – East of Acorn Street
Chestnut Street – East of Newton Street

## Slide 21: Plans

## Slide 25: Curb extension (Green area behind sidewalk)

## Slide 26: Raised intersection

## Slide 28: Questions and Comments

## Slide 29: Next steps:

## Slide 30
Source: Devon County Council Engineering and Planning traffic Calming Guidelines, U.K., 1991, p27

## Slide 31: Curb extensions