N.T.S. – All Specifications prepared for Cambridge Department of Public Works projects, regardless of type, size, and scope shall include this Section

SECTION 01105

# RODENT CONTROL

PART 1 - GENERAL

1.1	SUMMARY

A.	This section specifies rodent control and general pest control requirements within project areas, and bordering areas as designated by the Owner and Engineer.  This work is to be performed prior to demolition, excavation, and site preparation and throughout the Contract, so that rodents and other pests do not disperse from or infest the project area.

B.	The Contractor shall develop and implement an Integrated Pest Management (IPM) approach.  As part of that approach, the Contractor shall maintain a cooperative dialogue with appropriate agencies and management/representatives of neighboring properties.

C.	The Contractor shall perform the rodent control tasks described in this Scope of Work and also respond to other pest control needs when directed by the Owner.

1.2	SUBMITTALS

A.	Submit to the Engineer copies of pesticide applicator certifications and licenses within ten (10) days of the start of Rodent Control activities and ten (10) days prior to their issuance or renewal for the duration of this Contract.

B.	After performing the survey described in Paragraph 3.2 below and before initiating baiting, submit to the Engineer a written description of proposed pest control procedures, indicating materials, quantities, methods, and time schedule.  For all pesticides to be used, submit a copy of the pesticide manufacturer's EPA-approved pesticide label with application directions.

C.	Submit to the Engineer documentation of pest control activities and results and follows:

1.	Weekly - Submit data sheets with locations of sites treated, amounts and types of pesticide used, number and types of traps set, survey and inspection results, sanitation conditions, complaint calls investigated, and any problem that occurred.

2.	Monthly - Submit a written summary that includes determinable results of the IPM program and recommendations.

3.	Quarterly - Submit a map that shows bait stations, manholes, and catch basins where rodent baits are being maintained.

1.3	QUALIFICATIONS

A.	The Contractor shall perform this work at all times in accordance with the following minimum standards and as acceptable to the Owner and Engineer.

1.	The Contractor and key personnel shall have experience with commercial and residential accounts and construction projects; have experience and technical training in vertebrate pest management and integrated pest management; have experience with various rodent control techniques, equipment, and strategies; have training and experience with insect control; and have knowledge of and experience with techniques to reduce non-target hazards.

2.	The supervisor shall be licensed and certified by the Massachusetts Pesticide Bureau and certified in General Pest Control (category 41) and Vertebrate Pest Control (category 44).  The supervisor shall have specific training and experience in vertebrate pest management, commercial rodent control, general pest control, and integrated pest management.

3.	Applicators shall be licensed by the Massachusetts Pesticide Bureau and certified in General Pest Control (category 41).  Applicators shall have specific training and experience in commercial rodent control and integrated pest management.

1.4	COORDINATION

A.	Perform this Work in cooperation with the other Work performed under the Contract.

B.	Initiate the work on or before field mobilization begins for the Contract and with adequate timing to achieve control before environmental disruptions.  Provide a maintenance program until Contract is completed and all equipment and materials are removed.

C.	Perform the Work according to the preliminary schedule described in this section and as accepted or revised by the Owner and Engineer.  Estimated durations and start dates may be changed by the Owner or Engineer to suit changes in construction schedules and field conditions.  The Work could potentially require performance any day of the week and any hour of the day or night, regardless of weather.

D.	Perform this work in such a manner that toxicant or other control tools do no pose a hazard to persons, domestic animals, or non-target wildlife.

1.5	PERMITS

A.	Obtain and maintain in coordination with the Contractor appropriate permit(s) from city or state agencies for pest control activities associated with this Work.

B.	Obtain and maintain in coordination with the Contractor all right of entry permits required for the performance of this Work.  This includes all utilities and private properties to which entrance is required.

PART 2 - PRODUCTS

2.1	PRODUCTS

A.	Furnish and use only pesticide formulations registered by the U.S. Environmental Protection Agency (EPA) and the Massachusetts Department of Food and Agriculture, where appropriate according to label directions and as acceptable to the Engineer.

B.	Furnish and use devices and supplies (e.g., traps and bait stations) to facilitate the management and effectiveness of the pest control program, where appropriate and as acceptable to the Engineer.

PART 3 - EXECUTION

3.1	MEETINGS

A.	Before proceeding with the Work, all pest control personnel shall attend a Work Shop held by the Contractor and Engineer to discuss planned pest control methods and coordination.

B.	The supervisor shall meet with the Contractor and Engineer weekly to discuss pest control activities.

3.2	SURVEY

A.	Prior to baiting, survey the proposed construction area and accessible or observable bordering areas and record signs of rodent activity and sanitation conditions.  Closely inspect all embankments, edge areas, and properties within and abutting the construction area.  Maintain survey records in the manner described in Paragraph 3.7 below.

B.	Thoroughly inspect construction area and accessible or observable bordering areas and any nearby areas designated by the Owner or Engineer, for rodent activity and sanitation deficiencies weekly throughout the duration of this Contract and in accordance with the work schedule.  Maintain inspection records in the manner described in Paragraph 3.7 below.

C.	Plan the control program and allocate resources based on survey and inspection data and as acceptable to the Owner.

3.3	APPLICATION FOR RODENT CONTROL

A.	Apply rodenticide in strict accordance with EPA-approved label directions and the Rules and Regulations of the Massachusetts Department of Food and Agriculture.  Maintain records of all bait placements in the manner described in Paragraph 3.7 below.

B.	Where appropriate, especially for surface placements of rodent baits, use properly secured and tamper-resistant bait stations consistent with EPA regulation.  Individually number and properly identify all bait stations.

C.	Surface Applications

1.	Initial Surface Baiting

Rid the construction area of all detectable rodents before construction begins, or as acceptable to the Owner.  Bait all observable rodent burrows.  Install and secure bait stations at regular and appropriate intervals and locations, and document rodent activity (burrows, droppings, bait consumed, dead rodents).  Replenish bait and shift bait stations as necessary to ensure complete control of rodent populations.  Bait edge and accessible bordering areas as necessary to ensure that rodents will not be dispersed by construction activities and that rodents will not infest work areas.

2.	Maintenance Surface Baiting

Establish a maintenance baiting program prior to mobilization by the Contractor, including construction areas and accessible bordering areas, as acceptable to the Owner.  Check bait placements weekly.  Use survey and baiting data to determine the most effective distribution of baiting locations and bait quantities.  Shift and distribute bait and bait stations as appropriate to ensure continued control.

D.	Subsurface Applications

1.	General

For situations involving underground construction/demolition, utility relocation, or utility construction, and for other situations when determined necessary by the Owner or Engineer, initiate subsurface baiting and rid underground environments of all detectable rodents before construction begins.  Assign an identifying number to each manhole and catch basin where bait is placed so that locations of bait placements can be identified and rodent activity (droppings, bait consumed, dead rats) can be documented.  Conduct bait applications during off-peak traffic hours unless otherwise directed by the Engineer.  Access manholes according to the requirements of appropriate agencies and utility companies.  Coordinate the Work with appropriate municipal agencies and utility companies.

2.	Initial Subsurface Baiting

Apply appropriate baits to control rodent populations in manholes and catch basins.  This will involve suspending and securing bait using noncorrosive wire (e.g., 24 gauge plastic coated).  Place bait in all accessible manholes and catch basins within the construction work area.  In addition, bait an appropriate set of manholes and catch basins in the blocks bordering the work area and as acceptable to the Owner.  Identify all baited manholes and catch basins with a standardized paint mark on the street and a numbered tag to be attached to the suspending wire.  Approximately seven days after completion of the first baiting, check all manhole and catch basin baits and record estimates on the amount of bait consumed.  Replenish or increase the amount of bait applied according to the amount consumed or as acceptable to the Owner and Engineer.  Repeat this process again approximately fourteen days later and until there is little or no bait consumed.  Check manholes and catch basins weekly when they repeatedly have 100 percent of the bait consumed.

3.	Maintenance Subsurface Baiting

Prior to mobilization by the Contractor, establish a maintenance baiting program appropriate for the rodent infestation patterns identified during initial subsurface baiting.  This program shall ensure continued control and shall be performed in a manner acceptable to the Owner and Engineer.  Maintain bait in manholes and catch basins that have rodent activity and those that had activity during initial baitings.  Check each bait according to rodent activity levels.  This could range from weekly to approximately every three months, depending upon the recent history of bait consumption. Use utility maps and baiting data to determine the most effective distribution of baiting locations and bait quantities.  Shift and distribute baiting locations as necessary to ensure adequate interception points for controlling immigrating rodents.

E.	Cleanup

1.	Remove visible rodent carcasses and dispose of them daily consistent with the pesticide label directions and applicable codes, laws, and regulations.

2.	Upon completion of any pest control operations at the site, remove remaining bait and dispose of it according to the pesticide label and applicable codes, laws, and regulations.  Also remove all wires used for subsurface baiting and any bait stations or traps.

3.4	SANITATION

A.	Prior to construction and throughout the duration of this Contract, identify and document harborage and food sources available to rodents on the construction site and in observable bordering areas.  This includes any littering or improper or insufficient use of trash receptacles in construction areas.  It also includes any bordering areas with sanitation conditions or structural deficiencies that violate City or State sanitation codes.

B.	Maintain records of sanitation conditions in the manner described in Paragraph 3.7 below.

3.5	COMPLAINT CALLS

A.	During construction, respond to pest-related complaints from the "adjacent" neighborhood (i.e. within 200 feet of the project limits) within 12 hours when directed by the Owner or Engineer.  Inspect the particular premises and adjacent areas for sanitation and structural deficiencies and also signs of historic and recent pest activity.  Provide sanitation and structural maintenance information to the property owner or manager.  Use pesticides or traps as necessary and appropriate to resolve the complaint when there is a relationship between the pest infestation and construction activities, or when directed by the Owner or Engineer.

B.	Maintain records of all complaints investigated, including location, contact person, inspection results, and actions taken.  Document the relatedness of the pest infestation to construction activities.

3.6	GENERAL PEST CONTROL

A.	When directed by the Owner or Engineer, the Contractor shall determine appropriate methods for any pest control task not specifically identified above and shall submit them in writing to the Owner and Engineer for approval in advance.  Such pest control tasks would relate to unanticipated pest control needs within construction areas or adjacent areas.  This could include control of insects or vertebrates other than rats and mice.

B.	Maintain records of general pest control activities and results in the manner described in Paragraph 3.7 below.

3.7	RECORD KEEPING

A.	Use standardized data sheets acceptable to the Owner and Engineer to maintain accurate records of date, placement, type, and amount of pesticides or other control tools (e.g., traps) applied.  Similarly, maintain records of surveys, inspections, changes in pest activity, sanitation conditions, and complaint calls.  Submit data in a format acceptable to the Owner and Engineer and as required under Paragraph 1.3 (C) above.

PART 4 – Compensation

Not Used

END OF SECTION 01105

Jn